Let the name of your Python module be RVLPYTool.

1. Create a Python module in RVL/python/src as explained below. Let this module be defined in file RVLPYTool.cpp.
2. In makefile add

$(RVLPY_LIB_DIR)/RVLPYTool$(PYTHON_SUFFIX)

to variable LIBS (below comment “Output libraries”).

3. In makefile add

# RVLPYTool

$(RVLPY_LIB_DIR)/RVLPYTool$(PYTHON_SUFFIX): $(RVLPY_SRC_DIR)/RVLPYTool.cpp
@echo "Building RVLPYTool..."
${PYCC} $(RVLPYTOOL_INCLUDES) -L$(RVL_LIB_DIR) $(EXTERNAL_LIB_DIR) $< -o $@ $(RVLPYTOOL_LIBS)
@echo "RVLPYTool built."

where variables RVLPYTOOL_INCLUDES and RVLPYTOOL_LIBS must be defined before these lines.

4. make
5. You can make a demo Python script RVLPYToolDemo.py in directory RVL/python/build/lib.
6. Test the module by running script RVLPYToolDemo.py.

Creating Python Modules Using pybind11

Pybind11 (https://github.com/pybind/pybind11) is a tool for creating Python modules written in C++.
A Python module is created in a cpp-file.
After including all headers required by your module, add the following lines:

#include <pybind11/pybind11.h>
#include <pybind11/numpy.h>

namespace py = pybind11;

Create a wrapper class which will represent the interface between Python and your C++ code. Let the wrapper class be PYTool. Furthermore, let function1 and function2 be two member functions of PYTool.
At the end of your cpp-file add

PYBIND11_MODULE(RVLPYTool, m)
{
m.doc() = "RVL PYTool wrapper";

py::class_<PYTool>(m, "PYTool")
.def(py::init<>())
.def("function1", &PYTool::function1)
.def("function2", &PYTool::function2);
}